## Slide 1: Algorithm: Definition
An algorithm for solving a problem is a finite sequence of unambiguous, executable steps/instructions, which if followed would ultimately terminate and give the solution of the problem.
Finite set of steps:
Unambiguous:
Executable:
Terminate:
Hardware

## Slide 2: Hardware: Goals
Give physical realization of machines on which algorithms can be implemented
Some simple steps in the construction of a computer
To understand that the computers are essentially devices computing logical functions
To illustrate how complex systems can be built by incrementally realizing and putting together well defined parts.
To describe a computer as a general purpose machine

## Slide 3: Hardware
Input Devices
CPU
OutputDevices
Storage (Memory)

## Slide 4: Analogue/Digital Computer
Up to now whatever we have discussed could be discussed in context of analogue computation.
Now we will concentrate mostly on binary computer.
Why binary computers?
Physical components ---- transistors etc.
Reliability of hardware components.

## Slide 5: Binary Numbers
Decimal number system:
789 = 7102+ 8101 + 9100
Binary number system:
1001 = 123+ 022 + 021 + 120 = 9

## Slide 6: Decimal to Binary
43
43/2 -----> Quotient: 21 Remainder 1
21/2 -----> Quotient: 10 Remainder 1
10/2 -----> Quotient: 5 Remainder 0
5/2 -----> Quotient: 2 Remainder 1
2/2 -----> Quotient: 1 Remainder 0
1/2 -----> Quotient: 0 Remainder 1
(43)10 = (101011)2

## Slide 7: Decimal to Binary
n=(….bi…b0)2

## Slide 8: Binary Numbers
Using k bits, we can represent numbers from 0 to 2k-1 (if only doing non-negative numbers)
Addition, Subtraction etc on binary numbers in a way similar to that of decimal numbers
0+0 = 0
1+0 = 1
0+1 = 1
1+1 = 0 with carry 1
Example: Add 1011 and 1101

## Slide 9: Representation of Data
Numbers are not the only information that needs to be processes by computers.
Non numeric data
texts --- Roman alphabet, punctuation characters, etc.
ASCII: Codes for each symbol
It uses 7 bit code for each character
For example A is represented using 1000001.
Other data can be represented using binary numbers in similar way.
Instructions: ADD, SUB can be assigned codes.
Names of people, Sentences in a language.
Even analogue data can be represented using approximations.
Audio, Video ---> Via a process of digitization.

## Slide 10: Reasons for Using Binary Numbers
Reliability: Computers store information using electronic devices
===>
Internal representation using electronic quantities such as voltage, current, charge etc.
Building decimal computer would require 10 different distinct and stable levels.
For example: If voltage can vary between 0 and 90 volts. One may use 0, 10, 20, …. as different digits

## Slide 11: Reasons for Using Binary Numbers
Perfectly fine, in absence of other constraints.
Constraint: voltage is not reliable. Specially for old pieces of equipment. If a device storing 6 as 60Volts, loses 10% of its value, then the result is 54V or near the number 5.
Using binary number gives us much more error margin.

## Slide 12: Reasons for Using Binary Numbers
Additionally many devices have only two states:
magnetized/demagnetized
Charged/discharged capacitor

## Slide 13: Reasons for Using Binary Numbers
Problem gets more severe for real numbers.
Your CD player uses approximation and doesn’t represent exact frequency/volume etc. for audio
Your CD player still works because approximations are usually good enough: Your ear is not sensitive enough to notice the difference.
Once we have digital data, besides getting reliability we can apply other algorithms, for example compression, which makes it easier to handle the data.

## Slide 14: Boolean Algebra and Gates
Computer operations are based on logic circuits
Logic is based on Boolean Algebra
Logic Circuits have
  inputs (each with value 0 or 1 --- false or true)
  outputs
  state
Output depends only on input: Combinatorial Circuit
Basic building blocks for circuit: Gates
Combinatorial circuits are circuits formed using gates.
Output depends only on the input

## Slide 15: Gates
AND
Truth Table

## Slide 16: Gates
OR

## Slide 17: Gates
NOT

## Slide 18: Gates
NAND

## Slide 19: Gates
XOR

## Slide 20: Combinatorial Circuits
Half Adder
A circuit which adds two bits and produces sum and carry.
S=A B
C=A B

## Slide 21
Full Adder:
A circuit which adds two bits and a carry (from previous stage), and produces sum and carry (for next stage)

## Slide 23: Universality
It can shown that all combinatorial circuits can be realized using NAND gates only.
NAND is a UNIVERSAL gate.
Similarly using AND and NOT gates, one can build all combinatorial circuits.
How can we obtain Or gate using NAND gate?

## Slide 24: What goes inside a gate?
Gates need to be made of physical components.
Gates are made of what physicists call transistors.
A transistor is formed by sandwiching a p-type silicon between two n-type silicon or vice versa.

## Slide 25: Memory
Memory Element: Flip Flop. State: 0 or 1.
Change state: based on circuit at each TIME STEP.
Memory is the functional unit of computer that stores instructions and data.
Primary Memory:
RAM (Random Access Memory)
  read/write, volatile
ROM (Read only memory)
  read only, permanent
Memory is divided into fixed size units called cells.
Earlier no fixed size. Currently 8 bits --- called byte
Each memory cell has an address. Note that k bits can be used to address 2k memory cells/bytes.
For example, 10 address bits are needed to address 1024 (1KB) memory cells. 20 address bits for 1MB memory cells.

## Slide 26: Memory and Registers
Since Flip Flops have their state dependent on their previous state, they can be used in computers as memory elements.
A single Flip Flop is one bit of memory
A series of Flip Flops can be used to form a multi-bit memory
A register is a collection of basic memory cells. Essentially, it is similar to memory location, except that it is in the CPU itself (and thus can be accessed fast).

## Slide 27: Memory
Decoder circuits in memory is used to determine which memory location is being accessed. It is essentially a combinatorial circuit which converts the coded input address into output lines (one for each memory location) exactly one of which is 1, based on memory location being addressed.
Usually, two registers are used for accessing the memory.
MAR: Memory address register --- for address of the memory being accessed
MDR: Memory Data register --- for data to be written to the memory or read from the memory
Instructions fetch and store are used to read/write a memory location.

## Slide 28: CPU
What we need is a general purpose computer
Computer runs a STORED program.
This stored program can be arbitrary.
The basic architecture we discuss is called von-Neumann Architecture.

## Slide 29: CPU
We take a top level view.
Each subsystem can be built using logical circuits
This abstraction makes it easy to understand how the computer works.

## Slide 30: Example
To execute an instruction such as adding two numbers A and B, and placing the result in C, the following steps may be performed by the CPU:
1.Place the address of first number A in the Memory Address Register (MAR).
2. Issue a “fetch” instruction to the memory unit.
3. Transfer the contents of Memory Data Register (MDR) to register R1.
4. Place the address of second number B in MAR.
5. Issue a “fetch” instruction to the memory unit.
6. Transfer the contents of MDR to register R2.
7. Issue an instruction to the ALU to perform “addition” on R1 and R2, and place the result in R3.
8. Transfer the contents of R3 to MDR.
9. Place the address of C in MAR.
10. Issue a “store” instruction to the memory unit.

## Slide 31
Important Components of CPU:
Control Unit --- brain of the CPU. It decides which operations are to be performed and when.
Arithmetic Logic Unit (ALU): Consists of logical circuits for doing addition, multiplication etc.
Control signals are used to select which operation is to be done.
Buses: The buses are wires which connect different parts of the CPU and the parts of the CPU to other components of the computer.

## Slide 32
Instruction Execution:
CPU repeatedly executes the instruction cycle.
1. Fetch the instruction from memory
2. Decode the instruction
3. Execute the instruction (including the setting up for the next instruction to be executed)

## Slide 33
1. Fetch the instruction from memory
  Program Counter (PC) contains the address of next instruction
  Place the address on MAR
  Send fetch instruction
  Get the instruction from MDR
  Transfer to Instruction Register (IR)
2. Decode the instruction
  Generate list of micro instructions to be executed

## Slide 34
3. Execute the instruction (including the setting up for the next instruction to be executed)
  The sequencer keeps track of which microinstruction is to be executed in which order
  For example, for addition we need to send load instruction to the various registers, send instruction to ALU for adding, and then transfer the result to appropriate place, etc.
  Set up for next instruction to be executed
    Normally current instruction + 1
    May be different if control instructions (If then Else, etc.) are used

## Slide 35
Peripherals
--- Keyboard, Monitor, printers, speakers, etc.
--- disk drives, tapes (secondary memory)
I/O devices used vary a lot from computer to computer. Also one keeps adding/removing devices from the computer.
Easy addition/removal/replacement of I/O devices should be allowed.
Design of computer should be flexible to allow this.
This sometimes leads to suboptimal design. However it is better to have flexibility than optimality in such cases.